## Slide 1
Deep Learning - Design proposal

## Slide 2
Master/Deployer (8001-12C)
Ceph block
(OSD)
Ceph block
(OSD)
10 GbE
Lenovo G8264CS
1 GbE
Lenovo G8052
Compute - 8335-GTB
High Level Network Architecture Diagram
Per Compute Node
2x10G DAC Cables
2x 1G Cat5e Cables
2x10G
2x1G
OS provisioning
IPMI
Storage/Tensor
Customer Up-Links
EDR IB
Tensor
Optional EDR Infiniband
for Tensor communication
Storage – S822LC (8001-22C)
Storage
OS provisioning
IPMI
Per Storage Node
2x10G DAC Cables
2x 1G Cat5e Cables

## Slide 3
Management Server
Storage Server
NVLink Servers
Optional Infiniband

## Slide 4
Racking / Minimal Configuration
Rack:
QTY: 1
SlimRack 7965-94Y
PDUs
Network:
1 x Lenovo G8264CS (10G data network)
1*x Lenovo G8052 (1G management network)
Compute Node:
QTY: 3
Server Config:
Minsky 8335GTB (2U)
Processor – POWER8 10 Cores ( 3.492Ghz)
GPU – 4 x Nvidia GP100
Memory – 512 GB ,
2 x 3.8TB Sata HDDs
1 x PCIe2 10GbE SFP+ CU 4-port converged network adapter
Option: 3.2TB NVMe Flash Storage
Master/Deployment Node:
QTY: 1
Stratton S821LC (8001-12C)
Should support any Power8-LC system
Network Option:
1 x Mellanox (EDR IB data network)
Storage Node:
QTY: 1
Server Config:
Briggs 822LC (2U)
Processor – POWER8 10 Cores ( 3.492Ghz)
Memory – 256 GB ,
12 x 3.8TB Sata HDDs
1 x PCIe2 10GbE SFP+ CU 4-port converged network adapter

## Slide 5
Racking / Large Configuration
Rack:
QTY: 1
SlimRack 7965-94Y
PDUs
Network:
1 x Lenovo G8264CS (10G data network)
1*x Lenovo G8052 (1G management network)
Compute Node:
QTY: 8
Server Config:
Minsky 8335GTB (2U)
Processor – POWER8 10 Cores ( 3.492Ghz)
GPU – 4 x Nvidia GP100
Memory – 512 GB ,
2 x 3.8TB Sata HDDs
1 x PCIe2 10GbE SFP+ CU 4-port converged network adapter
Option: 3.2TB NVMe Flash Storage
Master/Deployment Node:
QTY: 1
Stratton S821LC (8001-12C)
Should support any Power8-LC system
Network Option:
1 x Mellanox (EDR IB data network)
Storage Node:
QTY: 1
Server Config:
Briggs 822LC (2U)
Processor – POWER8 10 Cores ( 3.492Ghz)
Memory – 256 GB ,
12 x 3.8TB Sata HDDs
1 x PCIe2 10GbE SFP+ CU 4-port converged network adapter